## Slide 1
Interface Block Diagram
Hardware Filtering Stage
Memory Mapped Registers
PIO_0 (24 bits)
24-bit data vector
Top 3 pixels in 3x3 window
PIO_1 (24 bits)
24-bit data vector
Middle 3 pixels in 3x3 window
PIO_2 (24 bits)
24-bit data vector
Bottom 3 pixels in 3x3 window
PIO_3 (16 bits)
16-bit ID vector
Identifies 3x3 window
PIO_4 (24 bits)
First 16 bits is the ID vector
Next 8 bits is the computed pixel
COMPSYS 701
Project Phase Two
Group 4
Operation
Convert 3x3 window into three 24-bit binary numbers, each composed of three 8-bit chars concatenated together
Write binary numbers to the data registers and a unique ID to the ID register
Wait for FPGA to write to the receive register
Use ID to place the receive char in the correct position
ARM Core
Avalon Bus AXI
filter_interface
Convolution Filter
PIO_0
PIO_1
PIO_2
PIO_3
PIO_4
24
24
16
24
Clk_50
24