## Slide 1: Designing an Object Detection System
Group 4

## Slide 2: Introduction
Hardware Trivium Solution
OpenCV Shape Detection
Hardware Filtering Solution
OpenCV Filtering

## Slide 3: Filtering
807s -> 465s

## Slide 4: Hardware Pipelining
465s -> 150s

## Slide 5: ID Tags
ID Tag – 8 bits
First 3 bits identify filter type
Last 5 bits is the number of the packet
0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1
ID Tag
Filter type
Packet number
Filter type bits | Filter
000 | Edge filter
001 | Gaussian filter
010 | Identity filter
011 | Median filter
100 | Sobel filter
101-111 | Reserved

## Slide 6: Object Detection
OpenCV libraries for C++
Modified software to compile using g++
Shape detection
Detects edges, determines if edges define a shape, determines what shape

## Slide 7: OpenCV Filtering
OpenCV libraries contain filtering functions
These functions are far faster than our hardware implementations
Sobel filtering twice in a row gives a blank image
150s -> 0.13s

## Slide 8: VGA Cache Access
Array was being accessed using a column-major logic
Caused a lot of cache misses since C uses row-major logic
Observed a time improvement of 13.82% afterwards

## Slide 9: Performance Improvements
Filtering Stage
  807s -> 465s -> 150s -> 0.13s
VGA Output Stage
  100s -> 87s
Total Run Time
  904s (1 FPS) -> 48s (19 FPS)
All measurements via gprof

## Slide 10: Future Work
Hardware filter daisy chaining
Multithreaded dual-core
24 bit colour
Luminance